## Slide 1: HPC400 Motor
Staffa Training
August 2016

## Slide 2: Agenda
HPC400
  Description
  Market position
  Design
  R&D Testing
  Performance
  Installation
  Model Code

## Slide 3: Description
4 displacement modes
Freewheel option available
Rated torque of 25,000 N m
Maximum continuous power of 430 kW
Dynamic displacement change
Based on HPC motor range with all latest developments included
Higher speed rating at full displacement

## Slide 4: Market Position
Aimed at marine winch market
  Increased power density
  Increased flexibility with 4 displacement modes
  Reduction of system complexity

## Slide 5: Design

## Slide 6: Design

## Slide 7: Design: C-Spacer

## Slide 8: Design: Valve Housing

## Slide 9: Design: Seal Technology
Shaft rings: new PEEK material with stainless steel spring backing rings
  Improved PV rating
  Improved leak rate
Displacement piston seals: new step-section rings
  Improved leak rate

## Slide 10: Design: Shaft
Double bank, each bank with high and low displacement
2 shaft options:
  Each bank with displacement range 5 in3/rev to 200 in3/rev
  Each bank with displacement range 0 in3/rev to 195 in3/rev

## Slide 11: Design: Motorcase
Standard motorcase – 10 bolt holes, Φ22mm
Different to B400 due to target market where acquiring 12.9 grade bolts may not be feasible
Where 12.9 grade bolts can be used, only 5 are required

## Slide 12: R&D Testing
2 million-cycle full power testing
Power testing with one drum in freewheel (zero-stroke)
Fatigue and burst testing for all new castings
Seal performance testing

## Slide 13: Performance
Significant gains compared to HPC range
  Continuous power rating improved
  Continuous speed rating improved
Displacements available – 10 in3/rev increments as standard. Others can be made as special parts
Datasheet performance figures limited at present – any figures not given available on request from Staffa Engineering Dept.

## Slide 14: Installation
CETOP3 displacement change only – no X-type
No vertical-up option at launch
Shaft seals: standard and high pressure
5 case drain holes
SFM45 valving only
C-spacer orientation at 2 o’clock and 10 o’clock as standard

## Slide 15: Installation
Displacement options: As current HPC motors, 10 cubic inch increments on each drum
Shaft options:
3D CAD models available on website

## Slide 16: Model Code